## Slide 1: Jittery Presentation
Daniel Sigg,
Commissioning Meeting, 11/11/16

## Slide 2: Why does PSL noise couple into the interferometer?
Intensity noise sensor after IMC
  At 10-20mW shot noise level below 1kHz
Frequency noise:
  Plenty of gain: FSS / IMC / REFL
Angular jitter:
But: Broad 500Hz hump at 50W (ang. jitter ruled out)
But: HPO/PMC length noise shows up in ifo much too strong (freq. & intensity coupling ruled out)

## Slide 3: HPO / PMC Connection
HPO produced huge amount of jitter
  But: After filtering thru PMC it is smaller than periscope/mount peaks at frequencies >100 Hz
  No indication that jitter below 100 Hz is a problem
  Still: Coherence between HPO jitter and DARM
More gain in HPO servo reduces peaks
  Injection locking servo (ILS) is gain limited
PMC:
  HPO peaks visible in error signal
  However: Increasing ugf will make peaks worse
  PMC length locking is limited by sensing noise (offset errors)

## Slide 4: PMC Length Noise Coupling
PMC length noise which corresponds to frequency noise at the 1Hz/√Hz level (at 1kHz) will show up in DARM
  Free running laser noise is higher (coupling thru freq. ruled out)
  Visible in ISS second loop, but too small (intensity noise ruled out)
  Visible in IMC WFS as jitter (jitter coupling too small & ruled out)
Not ruled out:
  Error point offsets into IMC or REFL; but how?
  Jitter by other higher order modes (e.g., beam size jitter)
  Polarization jitter
  Some (really) strange electronics pick-up

## Slide 5: Length Noise in Cavities Can Generate Jitter
Input field: TEM00 +ε Ex
  Ex can be TEMnm or Ep-pol
Cavity: TEM00 resonant
  Length noise will generate frequency noise on resonant mode
  Higher order modes will typically not be resonant and experience frequency shifts at a much smaller scale
  Transmission (PMC, IMC): higher order mode attenuated
  Reflection (all): no attenuation, used for reflection locking
Down stream frequency noise sensor
  The freq. stab. will remove any frequency noise on the carrier
  But will effectively imprint it on the higher order mode

## Slide 6: Higher Order Mode Coupling in Interferometer
A misaligned optics will shift carrier into TEM10
  Symmetric matrix: TEM10 jitter shifts to TEM00
  Same mechanism for curvature/beam size mismatch
  Differential arm cavity misalignment/curvature/size mismatch can generate AS port intensity noise
  Curvature/size mismatch fields can be 100x higher than misalignment
REFL port is vulnerable too
  Above mechanism works for RF modes too
  Generates error point offsets which will be imprinted on the frequency noise
  Frequency noise coupling above 100 Hz much higher than simple double cavity pole
  But signal is reduced by double cavity pole

## Slide 7: Closing Remarks
We do not meet the traditional beam jitter requirement
  Requires <1 nrad rms misalignment
  Jitter coupling seems to get worse with thermal loading
Do we need more filter cavities?
  In-air: double PMC on laser table
    Doesn’t solve the traditional jitter requirement
    Will eliminate HPO/PMC jitter noise
  In-vacuum: PMC style in HAM1(?)
    Will solve the jitter problem, odd mirror # will also reject polarization
    Will require in-vac modulators & relay optics
    IMC detector in vac?
Other options:
  Active mode matching?
  Active jitter suppression: hard to do with PZTs