## Slide 1
Laser Interferometer Gravitational-wave Observatory Where do we stand?
Daniel Sigg
LIGO Hanford Observatory
California Institute of Technology
GWADW 2017, May 8, 2017
For the LIGO Scientific Collaboration and the Virgo Collaboration
LIGO-G1700726-v2

## Slide 2
Stated Goals for O2 | How did we do?
Diagnose & reduce low frequency noise (f < 150 Hz) | Only small improvement on L1 Identified scattered light as needing work
Double the laser power (100 kW -> 200 kW arm power) | Got close with H1, but with a noise penalty
Work on transient noises and spectral lines | Some progress
More robust operation (low-noise duty cycle) | Definite payoff from suspensions dampers & seismic (tilt sensors)

## Slide 3
O1
O2
Volume-Time product now about the same for O1 & O2
Goal was 80-120 Mpc
2nd Observation Run
Start:
Dec 2016
End:
Aug 2017

## Slide 4
LHO High Power Work
~60 nm distortion over 20 mm
Hartmann Wavefront
Sensor Image of ITMX
Small point absorber (~10mW)
Resulting phase front distortion is problematic:
RF sideband build-up
Wavefront sensing
Noise couplings
Higher-order mode jitter!
PI damping successful (10 modes at 50W)
Thermal compensation worked
But: Noise worse at 50W

## Slide 5
LLO Scattered Light
End Stations: ETM wide angle scattering
‘Pcal Periscope Structure scattering’
Light scattered from the ETM is directed through a viewport and then scattered/reflected back in – hitting vibrating components along the way

## Slide 6
Stray Beams
A campaign to improve in-vacuum scattered light baffling in underway this will be one of the main post-O2 upgrades
View into HAM5 chamber
Signal recycling mirror
SR3: folding mirror in SRC

## Slide 7
Beam Jitter Coupling
Subtraction: J. Driggers
LHO has higher coupling
H1
L1
LHO alog 34631
Long term: May require Jitter Attenuation Cavity
  Fixed mirror
  Triangular, in vacuum
Suppression: ~50
Injection locked laser generates large amounts of beam jitter
Including higher order modes!

## Slide 8
Next Commissioning After the Run
Fix LHO-ITMX Contamination
  Will try to clean ITMX in early now
  If successful, will try to go back to 50W
  If unsuccessful, will require ITMX replacement after O2
Squeezed Light Injection at LLO
  Target is 3 dB of effective squeezing: equivalent to doubling the laser power
  Possibly LHO as well?
Stray Light Control Improvements
70 W Amplifier Stage at LLO to Double the Laser Power
  LHO: likely to move from the HPO to a 70 W amplifier as well
Replace End Reaction Masses with Annular Versions
  Squeezed film damping; possibly electro-static charge
  May also replace ETMs at LHO
Monolithic Signal Recycling Mirrors
LHO: Long vent

## Slide 9
Corner volume
HAM6 SLU
70 W amp
ERM swap
Cryo-pump decommissioning
Noise hunting
Power increase
Squeezed light injection
0
3
6
9
months
Corner volume
vent I
Diagnostics
Corner volume vent II
70W laser amplifier
ERM & ETM replacement
Noise hunting
Power increase
Thermal characterization
SRC alignment
Jitter Mitigation(?)
LLO
LHO
GV repair
Strawman Schedule
Depends on May vent
O3 readiness will be driven by achieving a significant sensitivity increase over O2

## Slide 10
Livingston Observatory

## Slide 11
Hanford Observatory

## Slide 12
40 cm
Test Mass Suspension

## Slide 13
Large Test Mass Optics
  Specifications:
  Diameter: 340 mm
  Thickness: 200 mm
  Mass: 39.6 kg
  ROC: 2250 m / 1940 m
  Figure: <1 nm rms
  Scatter: ~10 ppm
  Surface absorption: ~0.3 ppm
  Bulk absorption: ~0.2 ppm/cm
  HR transmission: ~4 ppm
  AR reflectivity: ~200 ppm

## Slide 14
Vacuum System Vertex

## Slide 15
Seismic Isolation Platform

## Slide 16
Input Optics Table

## Slide 17
200W Pre-Stabilized Laser

## Slide 18
Control Room