## Slide 1: The future of ground-based gravitational wave observatories
Sheila Rowan
University of Glasgow
GWIC Chair
Amaldi 2017

## Slide 2: Plans for the coming era of gravitational wave astronomy and astrophysics
In 2007/8 the international GW community formed a vision for the future of the field;
  2009 Gravitational Wave International Committee (GWIC) Roadmap: https://gwic.ligo.org/roadmap.
  Perspective: to optimize the global science in the field
  30-year horizon
  Global advanced detector network envisioned
2015 to now:
  start of the era of gravitational wave astronomy and astrophysics!
  Work of many 100s of people over several decades now paying off
  Long term thinking has been a hallmark of the field

## Slide 3: The global GW roadmap Circa 2009
We are here
From the Gravitational Wave International Committee (GWIC roadmap – available at: http://gwic.ligo.org/roadmap/ )
(InDIGO)
KAGRA
advLIGO
advVirgo
LCGT
GEO-HF
ET
US3G

## Slide 4: The global GW roadmap
We are here
From the Gravitational Wave International Committee (GWIC roadmap – available at: http://gwic.ligo.org/roadmap/ )
(InDIGO)
KAGRA
advLIGO
advVirgo
LCGT
GEO-HF
ET
US3G
Some timescales need revised but vision remains intact

## Slide 5: Sky localization with 3 sites …
Typical 90% error box areas for Neutron Star-Neutron Star binaries
  median > 20 sq deg
Fairhurst, CQG 28 105021 (2011)
LIGO-G1301140
Completing the advanced detector network
… and with 5 sites
c. 2020+
Notes: “localization accuracy for face on BNS at 160 MPc in various networks of advanced detectors. The ellipses contain the 90% localization regions for sources from various points in the sky. A × is plotted at points where the network would not confidently detect the system.”

## Slide 6: GW150914 Sky Location estimate

## Slide 7: Completing the advanced detector network
- LIGO-India

## Slide 8
LIGO-India 'in principle’ Approval
By Indian Union cabinet on Feb 17, 2016
… on a positive note with a BIG BANG !!!!

## Slide 9
LIGO-India: Indo-US MoU signed
Indo-US MOU between
Department of Atomic Energy &
Department of Science &Tech., India
and
National Science Foundation, USA
signed on March 31, 2016
at Washington DC
in the personal presence of
Hon. Prime Minister of India
LIGO-India selection
39 site leads followed up
(since Sept 2011)
Recommendation for primary and backup site Jul 2016
LIGO-India Site search
9
Led by IUCAA

## Slide 10
LIGO-India ‘preferred’ site
Maharashtra, India

## Slide 11
LIGO-India: site acquisition
Important Steps undertaken :
Formal letter from Secretary, DAE to State chief Secretary for Special project status : expected soon
Joint Measurement survey completed in Feb 2017
Restricted development zones 5km, 10km, 15km around LIGO-India implemented in district development plans
Payment of fees for initiating land acquisition procedure
Identification of land for LIGO-India campuses in neighbouring towns

## Slide 12: Buildup of Science
LIGO–India construction, installation and commissioning involve number of scientific issues
  Meeting stringent noise budgets in construction of infrastructure with regard to foundation, building design, installation of allied facilities.
  Scientific oversight of design, fabrication & installation of vacuum infrastructure
  Trained manpower for installation, commissioning, detector characterisation. Structured training program with LIGO USA & LSC.
  R&D to Advanced LIGO+ configuration in 2024.
  LIGO-India is expected to start in a much more advanced configuration than the advanced LIGO of 2015 or even 2018.
Creating a sizable science community commensurate with scale of LIGO-India megascience
Meeting LIGO–India promise for Indian S&T impetus.
See talk by Sanjit Mitra for more details

## Slide 13: Completing the advanced detector network
LIGO-India
KAGRA

## Slide 14: KAGRA Project
Host: ICRR UTokyo, Co-host: KEK, NAOJ
300+ collaborators from 90+ institutes
Constructed in Kamioka mine
Underground and cryogenic

## Slide 15
Super Kamiokande
Kamland
XMASS
3km
KAGRA
CLIO
CLIO
(GW)
KAGRA
(GW)
KAMLAND
(neutrino)
Suprer Kamiokande
(neutrino)
XMASS
(dark matter)
Office/
Control room
KAGRA entrance
Kamioka
220km
Tokyo
KAGRA is located in Kamioka mine underground
  220km away from Tokyo
  360m altitude
Big laboratory area

## Slide 16: Quiet underground site
ＴＡＭＡ３００
Surrounded by hard rock (Hida-gneiss)
  5 km/sec sound speed

## Slide 17: KAGRA Baseline Sensitivity
NSNS Range = 151Mpc

## Slide 18: Overall plan
Phase 1
Michelson with two cryogenic mirrors.
Initial KAGRA
Michelson at room temp.
Phase 2
Four cryogenic
mirrors.
Phase 3
DRFPMI with four cryogenic mirrors.
Observation run

## Slide 19: iKAGRA Test Run in 2016
Period: March 25 to 31 and April 11 to 25
obtain experiences of the management and operation of the km-class interferometer
test controls, data transfer, observation shift, etc.

## Slide 20: bKAGRA phase 1
PRM
PR2
PR3
SR3
SR2
ETMY
ETMX
BS
Mode Cleaner
IMMT
IFI
BRT
BRT
GW signal
Cryogenic Michelson Interferometer
Full scale suspensions
High power compatible input optics
Start operation by the end of March 2018

## Slide 21: Observation Scenario (Under discussion)
Binary neutron-star range:
25-40 Mpc in 2020,
40-140 Mpc in 2021
bKAGRA Phase 3

## Slide 22: Summary – KAGRA planning
iKAGRA: Initial 3km test run successfully done with very limited resources.
  Room temperature, simple Michelson, only one KAGRA style isolation system.
bKAGRA Phase 1 : The first cryogenic test run is planned in March 2018.
  Simple Michelson, two low temperature mirrors.
  Schedule is tight due to installations of KAGRA style isolation system.
bKAGRA Phase 2 : Two more cryogenic mirrors.
bKAGRA Phase 3: The first observation run in ~2020
See talk by Seiji Kawamura for news

## Slide 23: What Next?
Upgrades to Advanced detectors (keeping the current infrastructure)

## Slide 24: A bit of history
Evolution of the GW detectors:
2003
Infrastructure realization and detector assembling
2008
Same
infrastructure
Proof of the working principle
Upper Limit physics
2011
enhanceddetectors
Same
infrastructure
Test of “advanced” techs
UL physics
2017
Same
infrastructure
Advanced
detectors
First detection
Initial astrophysics
2022
Same
Infrastructure
(20 years old for Virgo, even more for LIGO & GEO600)
Commissioning
& first runs
Detection distance (a.u.)
year
Limit of the current infrastructures
A+, AdV+

## Slide 25
Key hardware improvements
Similar hardware features incorporated into LIGO-india, Advanced Virgo to give A+ global network?
(Advanced LIGO +)

## Slide 26
A+ Rationale

## Slide 27: A bit of history
Evolution of the GW detectors:
2003
Infrastructure realization and detector assembling
2008
Same
infrastructure
Proof of the working principle
Upper Limit physics
2011
enhanceddetectors
Same
infrastructure
Test of “advanced” techs
UL physics
2017
Same
infrastructure
Advanced
detectors
First detection
Initial astrophysics
2022
Same
Infrastructure
(20 years old for Virgo, even more for LIGO & GEO600)
Commissioning
& first runs
Precision Astrophysics
Cosmology
?
Detection distance (a.u.)
year
Limit of the current infrastructures
A+, AdV+
×10

## Slide 28: Limits of the Infrastructures?
Obsolescence
Length of the arms
Low frequency:
  Seismic and Newtonian noise
  Cryogenic apparatuses
Medium frequency:
  Size of the beam (thermal noise)
High/medium frequency:
  Long filtering cavities (squeezing)
Additional DoF:
  New geometries or topologies
  Multiple interferometers

## Slide 29: The Einstein Telescope design study
The “what next” question has been posed since 2004:
  ESF funded in 2005 an “Exploratory Workshop” on 3G GW observatories
    Design Study idea
Design study funded by the EC in FP7 (2008-2011)
  Involving France, Germany, Italy, the Netherlands, UK
Now the ET community includes also Hungary, Poland and Spain
Project included in sectorial roadmaps (GWIC, APPEC, OECD,. …) and worldwide recognized as leading 3G project

## Slide 30: The 3G/ET idea
To realise a 3G new GW observatory
  3G: Factor 10 better than advanced (2G) detectors
  New:
    We need new infrastructure because
      Current infrastructures will limit the sensitivity of future upgrades
      In 2030 current infrastructures may be tending towards obsolescence
  Observatory:
    Wide frequency, with special attention to low frequency (few HZ)
      Stellar mass Black Holes
    Capable to work alone (characteristic to be evaluated)
      Localization capability
      Polarisations
      High duty cycle: redundancy
    50-years lifetime of the infrastructure
      Capable to host the upgrades of the hosted detectors

## Slide 31: The Einstein Telescope

## Slide 32: Limits of the Infrastructures?
Obsolescence
Length of the arms
Low frequency:
  Seismic and Newtonian noise
  Cryogenic apparatuses
Medium frequency:
  Size of the beam (thermal noise)
High/medium frequency:
  Long filtering cavities (squeezing)
Additional DoF:
  New geometries or topologies
  Multiple interferometers
The path to 3G – adding in planning in the US

## Slide 33: GWIC 3G sub-committee
GWIC is conscious of the relevance of the global approach to 3G matters
A sub-committee has been formed to deal with this subject:
  Co-chairs: Dave Reitze, Michele Punturo
  Members:
  Federico Ferrini - EGO Director/interface to Virgo related
  organisations
  Takaaki Kajita - KAGRA Director
  Harald Lueck - interface to German agencies
  Jay Marx - Big Project Expertise
  David McClelland - interface to Australian agencies
  Michele Punturo - ET Design Study Lead
  David Reitze - LIGO Director/interface to NSF
  Sheila Rowan - GWIC Chair
D. Shoemaker (secretary)
V. Kalogera
B. Sathyaprakash
Expertise in astrophysics/analysis

## Slide 34: GWIC 3G sub-committee mandate
“Examining the path to a future network of observatories / facilities, specifically”:
1) Science Drivers for 3G detectors:
  commission a study of ground-based gravitational wave science from the global scientific community, investigating potential science vs architecture vs. network configuration vs. cost trade-offs, recognizing and taking into account existing studies for 3G projects (such as ET) as well as science overlap with the larger gravitational-wave spectrum.
2) Coordination of the Ground-based GW Community:
  develop and facilitate coordination mechanisms among the current and future planned and anticipated ground-based GW projects, including identification of common technologies and R&D activities as well as comparison of the specific technical approaches to 3G detectors. Possible support for coordination of 2G observing and 3G construction schedules.
3) Networking among Ground-based GW Community:
  organize and facilitate links between planned global 3G projects and other relevant scientific communities, including organizing:
    town hall meetings to survey the community (see later in this meeting)
    dedicated sessions in scientific conferences dedicated to GW physics and astronomy
    focused topical workshops within the relevant communities
WG under composition: chairs V. Kalogera, B. Sathyaprakash

## Slide 35: GWIC 3G sub-committee mandate
4) Agency interfacing and advocacy:
  identify and establish a communication channel with funding agencies who currently or may in the future support ground-based GW detectors; communicate as needed to those agencies officially through GWIC on the scientific needs, desires, and constraints from the communities and 3G projects (collected via 1) – 3) above) structured in a coherent framework; serve as an advocacy group for the communities and 3G projects with the funding agencies.
5) Investigate governance schemes:
  by applying knowledge of the diverse structures of the global GW community, propose a sustainable governance model for the management of detector construction and joint working, to support planning of 3rd generation observatories"
The subcommittee should provide a preliminary report and set of proposed actions recommendations to GWIC no later than the 2017 GWIC meeting.
Subsequent reports should be delivered future GWIC meetings.

## Slide 36: GWAC – Gravitational Wave Agency Correspondents
GW (“funding”) Agencies Committee
Promoted by NSF, involving:
  Australian Research Council (ARC)
  Canada Foundation for Innovation (CFI)
  Centre National de la Recherche Scientifique (CNRS)
  Consejo Nacional de Ciencia y Tecnología (CONACYT)
  Deutsche Forschungsgemeinschaft (DFG)
  Istituto Nazionale di Fisica Nucleare (INFN)
  National Aeronautics and Space Administration (NASA)
  Science & Technology Facilities Council (STFC)
  +++ open invitation to interested agencies

## Slide 37: Conclusions
GW detection is a wonderful achievement, but it is mainly the beginning of the new era of the GW astronomy and astrophysics.
New instruments will be needed to investigate the universe ( across the whole spectrum of gravitational wave sources)
New technologies and new infrastructures are needed for the future on the ground - and now it is time to articulate the science case, design and build them!
Thanks to Tarun Souradeep, Michele Punturo, Matt Evans, Mike Zucker, Osamu Miyakawa for slides