## Slide 1: LIGO: The Instruments that Launched Gravitational-wave Astronomy
Peter Fritschel, LIGO Laboratory
Massachusetts Institute of Technology
AAS 231st Meeting
Washington, DC
12 January 2018
LIGO-G1800030-v1
Image Credit: Aurore Simmonet/SSU

## Slide 2
± 1x10-21
± 5x10-22
± 3x10-22
± 6x10-22
30-250 Hz
35-400 Hz
30-200 Hz
30-200 Hz
24
13
13
18
Frequency
band
SNR
What have our detectors seen?
h =

## Slide 3: The BNS inspiral was rather different
Over ~100 sec, fgw 25  400 Hz
hp-p = 1x10-22
SNR = 32
This talk will describe the incredible detectors that made this collection of discoveries

## Slide 4: Detecting the effects of GWs
In a galaxy far far away…
(Earth)
GW’s produce time-varying transverse strain in space
 Monitor separations of free test particles
NGC4993
European Southern Observatory
Very Large Telescope

## Slide 5: Michelson interferometer
LASER
Beamsplitter
Photodetector
Inertial test body
Inertial test body
Lx
Ly

## Slide 6
A “small” problem…
A wave’s strength is measured by the strain induced in the detector 
We can calculate expected strain at Earth:
Our interferometer arms are 4,000 meters long,
!!
A ten-thousandth the size of an atomic nucleus

## Slide 7: The Enemies: NOISE
LASER
test body (mirror)
beamsplitter
Residual gas scattering
Wavelength & amplitude fluctuations
photodiode
Seismic Noise
Thermal (Brownian) Noise
Quantum Uncertainty
"Shot" noise
Radiation pressure

## Slide 8: Features of Interferometric GW Detectors
Frequency band for terrestrial detectors:
  ‘Unavoidable’ noises at low frequencies
  Detector response falls off as 1/f above a few hundred Hz
Interferometers have a broad directional response
10 Hz – 10 kHz
Antenna pattern for
unpolarized GWs
Arrival time triangulation
Nearly omnidirectional, but still useful for source localization
Binary neutron star detection
GW170817

## Slide 9: Brief history of LIGO
Original concept: 1972, Rai Weiss
Two observatories constructed from 1994 – 2000
  3 Interferometers:
  4 km & 2 km at Hanford
  4 km at Livingston
Initial LIGO operated from 2002 – 2007
Enhanced LIGO operated from 2008 – 2010
Reached design sensitivity, though no gravitational waves were detected
Caltech
MIT
3000 km (10 ms)
LIGO Livingston

## Slide 10
LIGO Hanford Observatory
H1 detector

## Slide 11
LIGO Livingston Observatory
L1 detector

## Slide 12: Built with the future in mind
4 km beam tubes were designed for the better vacuum needed by more sensitive interferometers
P = 10-9 torr
Vacuum chambers were designed to contain larger test masses
1.2 m diameter – avoid scattering against walls
Straight to fraction of a cm

## Slide 13: Enter Advanced LIGO
Installation
2011
Integration
Commissioning
L1
H1
O1
Advanced LIGO timeline
= first full lock
Project funding began in 2008
First observing run:
Sept 2015 – Jan 2016
An international partnership
Max Planck Institute (Germany): Laser
Science & Technology Facilities Council (UK): Suspensions
Australian Research Council: Sensors & controls
2012
2013
2014
2015
2016
2017
O2
Second:
Nov 2016 – Aug 2017

## Slide 14: LIGO Optical Configuration
end test mass
beam splitter
signal
Laser
Michelson
Interferometer
Light is “recycled” about 40 times
Power Recycled
input test mass
with Fabry-Perot Arm Cavities
Light bounces back and forth along arms about 100 times
signal recycling
& signal recycling
Advanced
Initial

## Slide 15: Advanced LIGO Optical Layout
In vacuum
In air
Up to 750 kw in each arm
So far, 100-120 kW
Gravitational wave, or
Medium power stage
High power stage

## Slide 16: It’s all about the sensitivity
Two common ways of characterizing sensitivity
frequency
Strain Noise Spectrum:
Since IFOs detect GW amplitude, plot amplitude spectral density of detector noise (square root of power spectrum), expressed as equivalent GW strain
ΔL/L,
per
Hz1/2
1
2
Inspiral Range:
the distance to which the coalescence of a pair of 1.4-solar mass neutron stars can be detected, averaged over direction and orientation
GW150914
quantum shot
noise
thermal noise
quantum
radiation
pressure &
seismic noise

## Slide 17: Strain Noise: O1 vs O2
L1 detector: O2 is 30-40% more sensitive than O1
  Using max available laser input power of 25 W
H1 detector: O2 is 5-10% less sensitive
  Laser power limited by excess absorption in one of the Input Test Masses
Hanford H1 Strain Sensitivity
Livingston L1 Strain Sensitivity

## Slide 18: H1 data can be improved
H1 had more contamination from auxiliary noise sources
  Largest culprit was laser beam motion, coupled with excess absorption in one of the test masses
These noise sources are monitored and can be removed with post-processing
  Performed on data around GW detections
Excess due to laser beam jitter

## Slide 19: Binary Neutron Star Inspiral Range
Goal for O2: > 80 Mpc BNS range for H1 and L1

## Slide 20: O2 Detector Duty Cycle
65%
62%
120 days

## Slide 21: Adv LIGO Target Design Sensitivity
Test mass coating thermal noise
Suspension thermal
Quantum
Gravity gradients
Seismic
Total noise
L1: O2

## Slide 22
Tour of the Detector

## Slide 23
Seismic Isolation Platform

## Slide 24: Seismic Isolation
Active suppression of sub-20 Hz vibrations
Motion of platform that supports test mass suspension
3-stage, 6 DoF active isolators

## Slide 25
40 cm
Test Mass Suspension
Main chain
Reaction chain

## Slide 26: Design for very low suspension thermal noise
Final stage of test mass suspension: all fused-silica, high quality factor to reduce thermal noise
Q ~1 billion
Test mass
Penultimate mass
Welded connection at the top
Welded connection at the bottom
60 cm of 400 micron silica fiber in between

## Slide 27: Test mass motion
Test mass seismic noise:
falling as f -11
Suspension thermal noise
30
4
3-stage active isolator
4 stages of passive isolation
20
6
8

## Slide 28
Test Mass
Very high Optical quality:
> a few 10’s ppm of total loss
> absorption of ≤ 0.5 ppm
Ultra-low-loss fused silica
34 cm φ x 20 cm thick, 40 kg
Super-polished + ion beam milling
  <0.15 nm RMS deviation from sphere
Mirror coatings:
  Ti:Ta2O5 / SiO2 multi-layers

## Slide 29
1 micron wavelength
Master Oscillator Power Amplifier
200 W pre-stabilized laser
Injection locked high-power oscillator
Frequency & intensity stabilization

## Slide 30
Future Plans

## Slide 31: Global network of detectors
VIRGO

## Slide 32: Near term prospects
Envisioned sensitivity evolution and observational runs
From LIGO-P1200087-v42
Currently preparing for O3

## Slide 33: Squeezed Light for O3
Squeezed light and squeezed vacuum
X1
X2
Squeezed light
Squeezed vacuum
X1
X2
X1
X2
Vacuum
fluctuations
X2
X1
∆X2
∆X1
Coherent
state of light
∆X1 ∆X2 ≥1

## Slide 34: Impact for O3 performance
x2 Higher power
x2 Higher power + squeezing
No further reduction of low frequency noise assumed in this plot
Squeezed light injection has essentially the same impact on quantum noise as increased laser power

## Slide 35
Beyond Advanced LIGO:
The A+ Upgrade
2020-2025

## Slide 36: A+: a mid-scale upgrade to Advanced LIGO
Improvements to quantum noise & thermal noise
Projected time scale for A+ operation: 2023-2025
A+
AdvLIGO design
BNS: 350 Mpc
BBH: 2250 Mpc
BNS: 175 Mpc
BBH: 1600 Mpc
O2

## Slide 37: Main elements of A+
New test masses with coatings that have lower thermal noise
  R&D in progress to find better materials
  Targeting a factor of 2 reduction in coating thermal noise
Higher levels of squeezing &
frequency dependent
2.5x
~100 m

## Slide 38: Final remarks
Advanced LIGO – the first of the 2nd generation detectors – launched GW astronomy in 2015
  Joined soon after by Virgo in 2017
Next Observing run with LIGO + Virgo starting near the end of 2018
  Sensitivity target for Binary Neutron Star mergers: 120+ Mpc
More coming
  KAGRA: start observing in 2020 with 25-40 Mpc range, 2021 with 40-140 Mpc range
  LIGO-India: to start observing in 2025

## Slide 39
LIGO Livingston Observatory
LIGO Hanford Observatory
LIGO Caltech
LIGO MIT
THANKS to:
My fellow Berkeley prize recipients
Dennis Coyne
Caltech
Chief Engineer,
Advanced LIGO/LIGO Lab
David Shoemaker
MIT
Advanced LIGO Project leader
Members of the LIGO Laboratory
Support:
National Science Foundation

## Slide 40: Extra slides

## Slide 41: Design limited by quantum & thermal noise
Quantum:
  well-established, depends on laser power & optical losses
Test mass thermal:
  dominated by Brownian noise of the mirror coatings; depends on materials properties that are not all well-known
  New experiment measures thermal noise directly on an AdvLIGO sample mirror
Coating thermal noise
Extrapolating to LIGO beam size:
Thermal noise is 20-25% higher than previous estimate
Target design BNS range reduced from 185 Mpc to 175 Mpc
S Gras, M Evans

## Slide 42
ADVANCED VIRGO
6 EU countries
20 labs, ~250 authors
APC Paris
ARTEMIS Nice
EGO Cascina
INFN Firenze-Urbino
INFN Genova
INFN Napoli
INFN Perugia
INFN Pisa
INFN Roma La Sapienza
INFN Roma Tor Vergata
INFN Trento-Padova
LAL Orsay – ESPCI Paris
LAPP Annecy
LKB Paris
LMA Lyon
NIKHEF Amsterdam
POLGRAW(Poland)
RADBOUD Uni. Nijmegen
RMKI Budapest
University of Valencia

## Slide 43: Advanced Virgo in a nutshell
Design is very similar to Adv LIGO
3 km arm length
Temporary configuration for O2
  No signal recycling
  Test masses suspended on metal wires

## Slide 44: KAGRA
Kamioka Underground SIte
22 cm
Cryogenic sapphire mirror & suspension
Currently working on cryogenic simple Michelson interferometer,
Operation spring 2018
3 km

## Slide 45: Major work being done on H1 & L1
Replace H1’s ITMX (excess absorption)
Stray Light Control improvements
70 W laser amplifier stage
  Goal is to double the operating laser power compared to O2
Replace End Test Masses & End Reaction Masses
  Better optical quality ETMs
  Reduce squeezed film gas damping with ERMs
Monolithic Signal Recycling Mirrors
Annular ERM
Old SRM
New SRM