## Slide 1: Ground-based Gravitational-wave detectors: Plans for the coming decade (and a bit beyond)
HEAD 2020
Chicago 20 March 2018
David Shoemaker
For the LIGO and Virgo Scientific Collaborations

## Slide 3: Ground based detectors
Initial observatories, and instruments, constructed starting in mid-90’s
  NSF Physics for LIGO; Virgo’s support from CNRS and INFN
Observed, setting upper limits until 2011
Both Virgo and LIGO undertook a complete rework of the instruments
Advanced LIGO came on line in 2015 – First discovery 15 Sept 2015
Advanced Virgo came on line in 2017 – First signal 14 August 2017
….then, on 17 August 2018….

## Slide 4
B. P. Abbott, Multi-messenger Observations of a Binary Neutron Star Merger, 2017, ApJL in press. doi:10.3847/2041-8213/aa91c9
Multimessenger Observations
Approximate timeline:
GW170817 - August 17, 2017 12:41:04 UTC = t0
GRB 170817A t0 + 2 sec
LIGO signal found t0 +6 minutes
LIGO-Virgo GCN reporting BNS signal associated with the time of the GRB t0 +41 minutes
SkyMap from LIGO-Virgo t0 + 4 hours
Optical counterpart found t0 + 11 hours
The localisation region became observable to telescopes in Chile 10 hours after the event time (wait for nightfall!)
Approximately 70 ground- and space- based observatories followed-up on this event
6

## Slide 5: Visual summary of signals to date

## Slide 6: Near Future: 2019-20
O2 – The Second Advanced detector Observing Run – was undertaken at 1/3-1/2 of the design sensitivity of the LIGO and Virgo instruments
Currently both LIGO and Virgo improving sensitivity of instruments:
  Introduction of higher laser power and use of ‘squeezed light’ (better high frequency performance)
  Changes in Virgo Suspension (better low-frequency performance)
  Better baffling/scattered light handling (better stationarity)
  (for Advanced LIGO, these are undertaken with LIGO Lab Operating funds, and anticipated as part of the commissioning)
Next: ~1 year long O3 run
  Start in Winter (late 2018/early 2019)
  LIGO with a NS-NS ‘reach’ of ~120 Mpc, Virgo ~65 Mpc
What can we expect from O3? Best guesses:
  BBH: Several per month to several per week
  BNS: 1 to 10 in the year-long run
  NSBH: N=0 not ruled out in any scenario, most give ~50% N>0

## Slide 7: 5-year plan

## Slide 8
8
8
The advanced GW detector network
Advanced
LIGO
Hanford,
Livingston
2015
Advanced
Virgo
2017
LIGO-India
2025
KAGRA
2019

## Slide 9
2025 Sensitivity/configuration:
5 detectors (add India and Japan)
far improved source localization
~60% in 10 sq deg
Notes: P0900125-v8

## Slide 10: Next LIGO Improvement: A+, ~2024

## Slide 11: A+ ‘elevator pitch’
An incremental upgrade to aLIGO that leverages existing technology and infrastructure, with minimal new investment and moderate risk
  Target: factor of 1.7 increase in range over aLIGO
  About a factor of 5 greater event rate (goes as the cube of sensitivity)
  “Scientific breakeven” within 1/2 year of operation
Could be observing within 6-7 years
Incremental cost: a small fraction of aLIGO -- NSF Mid-Scale Project
Requires some technical progress on
  High laser power handling
  Low optical losses
  Lower-mechanical loss optical coatings
    (our principal thermal noise source)
Sensitivity offers e.g., NSNS rates of 20-200 in a year observation
Proposal in preparation to NSF Physics and the UK STFC

## Slide 12: Evolution of detectors
aLIGO, AdV – commission to full sensitivity by early 2020’s
A+, AdV+ – add squeezing, lower thermal noise coatings; ~2024
Voyager – cryogenics to reduce thermal noise; ~2028
..at that point there is no choice but to seek longer arms
 Einstein Telescope
 Cosmic Explorer

## Slide 13: Not just about rates: With sensitivity comes new physics
Read, Schmidt, Clark and Lackey, G1700453
Read et al, Phys. Rev. D 88, 044042 (2013)
GW170817 limit

## Slide 14: Not just about rates: With sensitivity comes new physics
Read, Schmidt, Clark and Lackey, G1700453
Read et al, Phys. Rev. D 88, 044042 (2013)
Vanilla aLIGO limit

## Slide 15: Not just about rates: With sensitivity comes new physics
Read, Schmidt, Clark and Lackey, G1700453
Read et al, Phys. Rev. D 88, 044042 (2013)
3rd Gen limit

## Slide 16
Einstein Telescope
The next gravitational wave observatory
Coordinated effort with US to realize a
worldwide 3G network …
Conceptual Design Study

## Slide 17
Another Concept: Make Advanced LIGO 10x longer,
10x more sensitive
Signal grows with length – not most noise sources
Thermal noise, radiation pressure, seismic, Newtonian unchanged
Coating thermal noise improves faster than linearly with length
40km surface Observatory ‘toy’ baseline
  can still find sites, earthmoving feasible; costs another limit…
Concept offers sensitivity without new measurement challenges; could start at room temperature, modest laser power, etc.
Sigg et. al

## Slide 18: 3rd Generation
When could this new wave of ground instruments come into play?
Appears 15 years from t=0 is a feasible baseline
  Initial LIGO: 1989 proposal, and at design sensitivity 2005
  Advanced LIGO: 1999 White Paper, GW150914 in 2015
Modulo funding, could envision 2030’s
Should hope – and strive and plan – to have great instruments ready to ‘catch’ the end phase of binaries seen in LISA (ref. Sesana)
Worldwide community working together on concepts and the best observatory configuration for the science targets
Crucial for all these endeavors: to expand the scientific community planning on exploiting these instruments far beyond the GR/GW enclave
  Costs are like TMT/GMT/ELT – needs a comparable audience
  Events like GW170817 help!

## Slide 19
LIGO/Virgo
LISA
Pulsar Timing Array
Cosmology Probes
Just the beginning of a new field –
new instruments, new discoveries, new synergies

## Slide 20: Summary on Future planning
All ground-based interferometric detectors planning on working together – LIGO, LIGO-India, Virgo, KAGRA
  Sharing data, analysis development and execution
  Sharing instrument science technology development
  Coordinating on observing and upgrade schedules
Will share events via public alerts (GCN) with low latency to enable effective followup by EM/neutrino observers, Maximizing the joint MMA science
Incremental funding enables incremental improvements for the next decade
GWIC – the Gravitational Wave International Committee – coordinating development of ‘3rd Generation’ instrument concepts and approaches
  Explicitly global to ensure the best science, and best use of resources
  Refinement of the science case currently underway
  Governance models being explored
  Will look for support from the EM/neutrino Observers when seeking funding for major new infrastructures and instruments
Expect the GW Field to be a growing and reliable partner for EM and neutrino observatories and observers