## Slide 1: Improving earthquake monitoring for gravitational-wave detectors with historical seismic data
Sky Soltero
Mentor: Michael Coughlin
LIGO SURF final presentation
August 24th, 2018

## Slide 2: Agenda
Background
Neural Network
Comparing model results
Future work
LIGO facility in Hanford, Washington.
Current earthquake monitoring
Earthquake waves

## Slide 3: Earthquake Isolation
A level of isolation from the ground is required for Advanced gravitational-wave detectors such as the Laser Interferometer Gravitational-Wave Observatory (LIGO) to function at peak performance.
High magnitude teleseismic events can disrupt proper functioning, operation and duty cycle.
Less time in proper observation mode mean less gravitational waves being observed.
Which makes us very sad

## Slide 4: Earthquake Monitoring
With advanced warning of impeding tremors, the impact can be suppressed in the isolation system and the down time can be reduced at the expense of increased instrumental noise.
Is there a system in place that does this already?
YES!

## Slide 5: Implementation at the sites
An early warning system, called Seismon predicts the arrival times of earthquakes and the likelihood of the interferometer to go out of observing mode.
If there is high chance of losing lock, a trigger is made to change the control configuration at the interferometers using the LIGO automation system called Guardian.

## Slide 6: SEISMON
Seismon predicts the arrival time of the primary, secondary and surface waves of the earthquake
Predicts the likelihood for the interferometer to go out of observing mode and lose lock
Predictions are made using data from a worldwide network of seismic observatories compiled by the United States Geological Service (USGS)

## Slide 7
Before trying to better improve the arrival time predictions it’s necessary to understand Earthquakes better.

## Slide 8: Earthquake Arrival times
Earthquakes are detected when seismometers detect P-wave arrivals then initial estimates of magnitude and hypocenter are made
These preliminary estimates can then be made more accurate with S-wave and surface wave arrivals

## Slide 9: Waves 101
S- waves
P-waves
Solids
Shears rock sideways
1-8 km/s
Solids and liquids
Compresses and dilates
1-14 km/s
Occurs on crust
Love: side to side
Rayleigh: rolling
2-6 km/s

## Slide 10: P and surface wave comparison
P-waves travel at about twice the speed of surface waves

## Slide 11: P- waves
Higher P-wave speeds are often due to the location and azimuth degree

## Slide 12: Improving predictions with a Neural Network
A Neural network was created to improve the arrival time predictions along with ground velocity and detector status
Using past historical data from the detectors at Hanford, Livingston, VIRGO and the large collection of IRIS data
Earthquake Magnitude
Latitude
Longitude
Distance (m)
Depth (m)
Azimuth (deg)
Arrival Times
OR
Ground Velocity
OR
Detector Status

## Slide 13: Hyper-parameters
Experimented with the amount of hidden layers and various Hyper-parameters
Best result models were then saved for predicting arrival times, ground velocity and detector status
Models were also trained on different historical data sets

## Slide 14: Hanford vs. Livingston vs. VIRGO Arrival time
These datasets were filter to not include earthquakes with a ground velocity smaller than a micrometer (μ) per second.
HANFORD
LIVINGSTON
VIRGO

## Slide 15: IRIS data
Earthquakes data at the detectors was small (2000-3000 Earthquakes)
Utilized earthquake data collected at Incorporated Research Institutions for Seismology (IRIS) (+730,000 Earthquakes)
Filtered the data to include only earthquakes originating around the United States

## Slide 16: IRIS Arrival time
Cut earthquakes with a ground velocity less than a micrometer (μ) per second.
IRIS data includes P-waves
Cut earthquakes greater than > 6000 m/s to try and limit P-wave contamination
Cut earthquakes not originating on land
Reduced to about 29,600 EQS

## Slide 17: Neural Network models
When training a Neural Network a randomized portion of data is set as the training set and another portion as the testing set.
Can save Neural network model with particular architecture and weights
What happens if we train a model on a portion of one dataset and test it on the complete data set of another?

## Slide 18: Arrival times Trained models on other data sets
 | IRIS TRAINED TRAINED | HANFORD TRAINED | LIVINGSTON TRAINED | VIRGO TRAINED
IRIS TESTED
HANFORD
TESTED
LIVINGSTON TESTED
VIRGO TESTED

## Slide 19: Arrival times
What happens if the model is trained with data omitting earthquakes with velocities > 6000 m/s?

## Slide 20: Arrival times
What happens if the model is trained with data omitting earthquakes with velocities > 6000 m/s?
Hanford trained:
Velocities <6000m/s
Hanford tested:
Velocities <6000m/s
Hanford trained:
Velocities <6000m/s
Hanford tested:
All velocities

## Slide 21: Detector Status Neural Network
Detector status was hardest to predict
Can’t use IRIS data or Virgo data
Predicting classes > loss: categorical_crossentropy
K-fold Cross-evaluation to evaluate model accuracy
Confusion matrix to present results
0:Not Locked
1:Locked but can’t take data
2: Locked but lost lock

## Slide 22: Lets make some predictions!
Script written to take in neural network models, different data sets (or one earthquake’s data) and make predictions
PREDICTIONS
ARRIVAL TIMES,
GROUND VELOCITES,
DETECTOR STATUS
Arrival Times Model
Ground Velocity
Model
Detector Status Model
Earthquake Data
Earthquake
Magnitude
Latitude
Longitude
Distance (m)
Depth (m)
Azimuth (deg)

## Slide 23: FUTURE WORK
Improving the models further with hyper tuning, grid searches and random searches
Combining Hanford, Livingston, and VIRGO data to train network
Filter out high frequencies of IRIS data
Determining if including all of IRIS data OR further filtering along different parameters can improve model training and predictions
Implementing prediction models into Seismon pipeline

## Slide 24: Acknowledgements
THANK YOU!
MICHAEL COUGHLIN
LIGO CALTECH
CALTECH SFP
CSUF GWPAC
LIGO SURF

## Slide 25: Extra Slides

## Slide 26: Neural Network Specifics: Arrival times (IRIS trained)
Lr:1e-3
Reg: 0.0
Dropout: 0.2
Layers: 7 Dense layers of 64 nodes
Activation:relu
Epochs:500
Batch Size: 32
Optimizer: Adam
Loss=mse.

## Slide 27: IRIS Ground velocity Trained and Tested
Cuts were made:
Ground velocities >micrometer
Velocity <6000
Only land points

## Slide 28: Models on iris data (No data input cuts)
Hanford Livingston Virgo

## Slide 29: Ground Velocity Trained models on other data sets
 | IRIS TRAINED | HANFORD TRAINED | LIVINGSTON TRAINED | VIRGO TRAINED
IRIS TESTED
HANFORD
TESTED
LIVINGSTON TESTED
VIRGO TESTED

## Slide 30: Detector Status Trained models on other data sets
 |  | HANFORD TRAINED | LIVINGSTON TRAINED | 
HANFORD TESTED |  |  |  | 
LIVINGSTON TESTED |  |  |  |