## Slide 1: LIGO's past and future observations of Black Hole and Neutron Star Binaries
Marcel Grossmann, Rome
3 July 2018
David Shoemaker
For the LIGO and Virgo Scientific Collaborations
Credits
Measurement results: LIGO/Virgo Collaborations,
PRL 116, 061102 (2016); Phys. Rev. Lett. 119, 161101 (2017);
Phys. Rev. Lett. 119, 141101 (2017); Phys. Rev. Lett. 118, 221101 (2017);
Phys. Rev. Lett. 116, 241103 (2016)
Simulations: SXS Collaboration; LIGO Laboratory
Slides from (among others) L. Nuttall, P. Fritschel, L. Cadonati, P. Shawhan, A. Nitz, L. Singer
Photographs: LIGO Laboratory; MIT; Caltech; Virgo
LIGO thanks the NSF for its vision and support!

## Slide 2
Observe together as a Network of GW detectors
Coordinated talks –
  Today: Detection and analysis principles (David Shoemaker, LSC)
  Tomorrow: Physics, Astrophysics, and the Future (Jo van den Brand, Virgo)

## Slide 3: What is our measurement technique?
Enhanced Michelson interferometers
  LIGO, Virgo use variations
GWs modulate the distance between the end test mass and the beam splitter
The interferometer acts as a transducer, turning GWs into photocurrent proportional to the strain amplitude
Arms are short compared to our GW wavelengths, so longer arms make bigger signals  multi-km installations
Magnitude of h at Earth:
  Detectable signals h ~ 10-21
  (1 hair / Alpha Centauri)
  For L = 1 m, ΔL= 10-21 m
  For L = 4km, ΔL= 4x10-18 m

## Slide 4: Adv LIGO Target Design Sensitivity, basic noise sources
Test mass coating thermal noise
Suspension thermal
Quantum
Gravity gradients
Seismic
Total noise
L1: O2

## Slide 5: LIGO Sensitivity for first Observing runs
Initial LIGO
O1 aLIGO
Design aLIGO
Broadband,
Factor ~3 improvement
At ~40 Hz, Factor ~100 improvement

## Slide 6: Final Slide from my talk at MG 14 August 2015:

## Slide 7: The first signal came one month later
September 14, 2015, seen at the two LIGO observatories
  Delay between the two of 6.9 msec removed in plot below
Binary Black Hole inspiral; assuming GR, best fit 36, 29 M⦿, 410 Mpc
 1/10 second 

## Slide 8: How do we prepare and analyze data?
Discuss only binary inspirals here
  Burst, Continuous Wave, and Stochastic have different approaches
Assume GR is correct for the search
Ideal detector noise would be stationary, Gaussian, and uncorrelated between the two detectors
In reality, none of these properties hold exactly for LIGO data; our data analysis searches are crafted to be robust against these characteristics
More information for those interested in the details can be found in materials for an Open Data Workshop held – https://losc.ligo.org/s/workshop1/course.html

## Slide 9: Forming the PSD: Windowing
To create the efficient template bank we need to know the Power Spectral Density (PSD) of the detector noise
The discrete Fourier transform assumes that data are periodic
Real detector data are not periodic as the last point in one segment of data, sN-1 , will be correlated with the 1st point of the next segment of data, sN , but not the first point of the segment of data
A standard technique to partially mitigate the artificial imposition of periodicity is to window the data segment
The phases of the discrete Fourier transform of the LIGO noise at Hanford, WA (H1) at the time of GW150914
The phase spectrum of 32 s of unwindowed data.
The phase spectrum of the same data after applying a Hann window

## Slide 10: Making a set of search templates
Construct a stochastically-distributed set of templates based on GR
  Component mass of each object in the 'detector frame' (i.e., redshifted)
  Spin aligned with the orbital angular momentum
  Only the dominant mode (spherical harmonics)
Require that we would lose no more than 10% of signals anywhere in our parameter space
 ~250,000 templates
Added more high-mass templates after GW150914!

## Slide 11: Remove clearly defective data
Many causes and indicators
  External seismic disturbances
  Internal mechanical stress release
  Signals in excess of dynamic range

## Slide 12: Matched Filter

## Slide 13: Matched Filter

## Slide 14: Quasi-stationary Noise around GW150914
The noise is colored (Seismic, Thermal, photon shot noise)
There are carefully-studied narrow line-like features also:
  Digital acquisition (can be GPS synchronized between detectors)
  Harmonics of the 60 Hz power lines (again, synch. Possible)
  Resonant modes of the suspension systems
  Calibration lines
  Acoustic pickup
These are suppressed by orders of magnitude by the optimal matched filtering process

## Slide 15: Quasi-stationary Noise around GW150914
The noise is colored (Seismic, Thermal, photon shot noise)
There are carefully-studied narrow line-like features also:
  Digital acquisition (can be GPS synchronized between detectors)
  Harmonics of the 60 Hz power lines (again, synch. Possible)
  Resonant modes of the suspension systems
  Calibration lines
  Acoustic pickup
These are suppressed by orders of magnitude by the optimal matched filtering process
The square of the inverse of the amplitude spectrum

## Slide 16: Non-stationary noise
Require that the Signal is…:
Seen in multiple detectors within light travel time between the observatories
Relative amplitude and phase of observed signal consistent with a single astrophysical source
Signal morphology be consistent between observatories
Consistency between signal model and observed data
  SNR contribution by frequency band
  Autocorrelation function
  SNR distribution over template bank
Transient instrumental noise excitations – Glitches – must be excluded
Check over 200 000 auxiliary channels
  motion of the ground or optics tables, magnetic and electric field variations, acoustic disturbances, or cosmic ray showers
  Couplings are determined via excitation

## Slide 17: Require that the signal is internally consistent
Re-weight the SNR by a time-frequency test of signal consistency
For each maximum we calculate a chi-squared statistic to test whether the data in several different frequency bands are consistent with the matching template
This gives a powerful veto of noise pulses which start out looking like an inspiral but deviate shortly thereafter

## Slide 18: Estimate the Significance
We time shift the data of one detector relative to the other
Coincidences in time slides are background triggers
Any correlations in the background noise of the two detectors would show up here as peaks in time slides
IF the proper windowing, rejection of defective data, and optimal filtering is applied, no anomalous correlations are observed – just random coincidences
This process assures that the estimation of significance takes into account our non-Gaussian, non-stationary noise

## Slide 19: Test the system
Inject hundreds of thousands of test signals in software
See that the multiple, independently- developed pipelines find the signals and characterize them correctly
  No accidental software injection could be confused with a real event; a real event shows up in many internal channels
We do perform some hardware signal injections in an end-to-end test
  These are not ‘blind’ – they are announced, and the excitation signal is clear in the monitoring channels
  No accidental (or nefarious) hardware injection could sneak in; the excitation channels are checked as part of the detection process, experimental spaces monitored with video, electronics safety-taped shut
By the way – our hardware injection actuator does not have enough high-frequency power to hardware-inject a binary neutron star inspiral!

## Slide 20: Success!
A valid signal survives all these processes and tests
Can proceed with parameter estimation, inferences about physics

## Slide 21: O1-O2 Data
Completing search on the O2 data
Catalog of all events in preparation
Other searches (Burst, Continuous Wave, Stochastic) also in process
  Continuous Wave searches are particularly compute- and so time-intensive
Per the Data Management Plan, the strain data from the entire O2 run will be released in February 2019
  Look forward to independent analysis and perhaps discoveries

## Slide 22: Speaking of analysis of LIGO Data
GWOSC (https://losc.ligo.org/about/ ) hosts
  GW strain data around the time of each reported event
  Event localization (SkyMaps)
  Full Data sets (all O1 data now there; O2 data in Feb 2019)
  Tutorials – please note, these are demonstration analysis programs, not those we use
  Software links for much of our production software
    ‘PyCBC’, one of the inspiral analysis pipelines is now well packaged
Intend for it to grow in detail and scope

## Slide 23: Speaking of analysis of LIGO Data
LSC and Virgo are glad to see analyses of GW data beyond the Collaborations
  Tests of confidence in results, alternative approaches
  Searches for events the LVC did not find
  Searches for hypothesized event types not targeted by LVC
  Growth in the field
Papers appearing using data from GWOSC
Growing list compiled at https://losc.ligo.org/projects/
Input from community helping us adjust how we provide derived data, providing insights – e.g.:
  As Creswell et al. found, figure in GW150914 PRL did not have exact residuals
  Now adding posterior samples from parameter estimation (not in LIGO Data Management Plan)

## Slide 25: What else have we seen? Focus on two events jointly detected by Virgo and LIGO

## Slide 26: GW170814
B. P. Abbott et al., A Three-Detector Observation of Gravitational Waves from a Binary Black Hole Coalescence, 2017, Phys. Rev. Lett., 119, 141101
The first GW signal observed by LIGO-Hanford, LIGO-Livingston and Virgo
12

## Slide 27
Skymap enabled with GW170814
Skymap area reduced ~20x
Virgo
Hanford
Livingston
Volume reduced ~34x
13

## Slide 28: Forming the Sky map
Analysis treats the detectors as phased array antenna (aperture synthesis)
Localization of short-duration GW signals requires coherent consistency among the data recorded by the different detectors
  The antennas have known sensitivity patterns for each polarization that are slowly varying functions of direction
  The waves come in a linear combination of two polarizations
  The relative times, phases, and amplitudes on arrival at all of the antennas depend on the relative positions and orientations of the source and all of the antennas
  We determine the location of the source by “phasing up” the antennas for a particular direction and comparing with what was actually received, then repeating for all directions on the sky.
Leo Singer

## Slide 29: One more detection: GW170817

## Slide 30: One more detection: GW170817

## Slide 31: Glitch in Livingston data
Time-frequency representation of the raw LIGO-Livingston data
Raw LIGO-Livingston strain data
Grey: Gating veto window for skymap produced ~4.5h after the event
Blue: model subtracted from data for parameter estimation later

## Slide 32: One more detection: GW170817

## Slide 33: Antenna pattern for a single detector
Maximal for overhead or underfoot source
1/2 for signals along one arm
…and zero at 45 degrees
GW170817 fell on Virgo close to 45 degrees
Did no harm for localization, given our ‘aperture synthesis’ approach. (GW170814 proved the detector was working)

## Slide 34
GRB 170817A
GRB 170817A occurs (1.74 ± 0.05) seconds after GW170817
It was autonomously detected in-orbit by Fermi-GBM (GCN was issued 14s after GRB) and in the routine followup search for short transients by INTEGRAL SPI-ACS
Probability that GW170817 and GRB 170817A occurred this close in time and with location agreement by chance is 5.0x10-8 (Gaussian equivalent significance of 5.3σ)
BNS mergers are progenitors of
(at least some) SGRBs
B. P. Abbott et al., Gravitational Waves and Gamma Rays from a Binary Neutron Star Merger: GW170817 and GRB 170817A, 2017, ApJL 848, L13
3

## Slide 35: Chronology of GW170817
12:41:04 - Event time at Earth
12:41:06 - Low significance GRB trigger from Fermi
12:47:18 - gstlal uploads an H1-only trigger with a FAR=3.5 x 10-12 Hz
12:47:22 - RAVEN algorithm initiates coincidence search GW-GRB
12:47:31 - RAVEN finds coincidence, improves FAR to 1.95e-16 Hz
12:58:25 - Chad Hanna applies the ADVREQ label to the event.
12:59:29 - Label H1OPS is applied by Observatory
12:59:46 - Label L1OPS is applied by Observatory
13:00:07 - Label V1OPS is applied by Observatory
13:03:11 - Nicolas Menzione applies the V1OK label
13:05:47 - Alan Weinstein applies the ADVOK label
13:08:15 - First machine-readable alert sent. To + 27 minutes
13:08:09 - Marc (Doug) Lormand applies the L1OK label
13:17:33 - Corey Gray applies the H1OK label
13:21:42 - GCN 21505 sent by LIGO and Virgo collaborations
13:47:37 - GCN 21506: GBM-LIGO Group reports on the time-coincident GRB
17:54:51 - GCN 21513 with the H1,L1,V1 map. T0 + 5h14m
17/08/18 01:05:23 - Swope GCN 21529 Optical counterpart T0 + 11 hours
A handful of very excited observers preparing their searches
A handful of very excited GW scientists looking at data

## Slide 37: GW170817 Followup Observations
No need for me to say anything on this!

## Slide 38: LIGO Scientific Collaboration and Virgo Collaboration
~1500 members, ~120 institutions, 21 countries
19

## Slide 39: What does the future hold?

## Slide 40: Plausible Observing Timeline
Binary Neutron Star Range
Adapted from B. P. Abbott et al., Prospects for Observing and Localizing Gravitational-Wave Transients with Advanced LIGO, Advanced Virgo and KAGRA, 2016, Living Rev. Relativity 19
18
173
Mpc

## Slide 41: The O3 Observing Run
Current start date February 2019
Duration roughly one calendar year
Engineering runs in ~October and ~January
LIGO and Virgo synchronized, sharing real-time data
  Joint alerts, MoUs, publications
KAGRA may join toward end of O3
LIGO instruments 120 Mpc (BNS, SNR 8, averaged)
Virgo: 20  60 Mpc
 Network ~x2 better
Better SNR for a given source; more detailed information, less ambiguity
Greater reach, higher rates

## Slide 42: Rates in O3
From Town Hall presentations
Chris Pankow

## Slide 43: Once O3 is running, ~February 2019:
Fundamental change for O3: Open Public Alerts for Triggers
  No more standard EM follow-up MOUs or private GCN alerts!
  LIGO/Virgo to release public alerts for all event candidates for which we have reasonable confidence
    For binary mergers: target 9 out of 10 valid
    More restrictive threshold for unmodeled GW burst candidates
    We can “promote” a weaker GW candidate if it is coincident with a GRB, core-collapse supernova, etc.
  We’ll provide basically the same information as in O2: significance, time, binary type classification, sky position and distance 3D map
    Considering adding some more information to aid prioritization
  We’ll provide automatic preliminary alerts before human vetting – goal is to provid this within minutes
See https://www.ligo.org/scientists/GWEMalerts.php for more info

## Slide 44: LIGO Roadmap: A+
173
Mpc
O4
A+ Install
Commission
44
An incremental upgrade to aLIGO that leverages existing technology and infrastructure, with minimal new investment, and moderate risk
Target: factor of 1.7 increase in range over aLIGO
About a factor of 4-7 greater CBC event rate
Stepping stone to third-generation (3G) detector technology
Bridge to future 3G GW astrophysics, cosmology, and nuclear physics
Can be observing within 6 years (mid-2024)
– Jo van den Brand will talk about the further future tomorrow.

## Slide 45
45
45
A bright future for a new field
Advanced
LIGO
Hanford,
Livingston
2015
Advanced
Virgo
2016
LIGO-India
2025
KAGRA
2019