## Slide 1: Can you get there from here? Thinking about paths from AdV+/A+ to 3 G
D. McClelland, M. Zucker
Dawn IV
30-31 August 2018
LIGO-G1801680

## Slide 2: Outline
Perspective on A+
    Can someone offer symmetrical view for AdV+? Sorry, was planning to do more homework.
Constraints: real vs. imagined
“Baby steps” vs. “Giant Leaps”
Some ideas

## Slide 3: A+ ‘elevator pitch’ (we’ll come back to this later)
An incremental upgrade to aLIGO that leverages existing technology and infrastructure, with minimal new investment, and moderate risk
Target: factor of 1.7* increase in range over aLIGO
About a factor of 4-7 greater CBC event rate
Bridge to future 3G GW astrophysics, cosmology, and nuclear physics
Stepping stone to 3G detector technology
Can be observing within 6 years (mid- 2024)
“Scientific breakeven” within 1/2 year of operation
Incremental cost: a small increment on aLIGO
Joint international effort: ~ 35% UK and Australia funding
*BBH 30/30 M: 1.6x
*BNS 1.4/1.4 M: 1.9x

## Slide 4: A+: a mid-scale upgrade to Advanced LIGO
Reduced quantum noise
  Improved optical losses
  Improved readout
  Frequency-Dependent Squeezing
Reduced thermal noise
  Improved mirror coatings
Observing by mid-2024
A+
aLIGO design
BNS: 325 Mpc
BBH: 2563 Mpc
BNS: 173 Mpc
BBH: 1607 Mpc
O2

## Slide 5
Based on P170608 and P170817 rate density estimates:
BBH rate 4.1x aLIGO  17-300 BBH/month
Off-axis observations  BH component spins
BH Spins  Origins of stellar-mass BH
Zmax ~ 1.5  BBH cosmological evolution
SNR ~ 100  Ultra-precision tests of GR
BNS rate 6.7x aLIGO  1-13 BNS/month
(2-11 BNS x SGRB coincidences/year)*
Multimessenger coincidences  precision H0 measurement, kilonovae, etc.
High inspiral SNR  BNS tidal deformation
BNS remnant “ringdown”  NS matter equation of state
*(or more, if GW170817 represents hidden sub-threshold SGRB population)
Selected A+ Discovery Targets

## Slide 6
S. Vitale, M1800040
Figure 7: Redshift distribution of binary black hole sources detectable with SNR > 10 in a single A+ detector, as compared to baseline aLIGO at design sensitivity.

## Slide 7: BNS post-merger “ringing” vs. NS EOS
Figure 6: BNS post-merger signal models vs. aLIGO and A+ detector noise for a range of speculated neutron-star equations of state (labeled 2H - B). A+ will have significantly improved capacity to detect post-merger "ringing" modes, whose characteristic frequencies are determined by the equation of state of super-nuclear matter. The low-frequency inspiral waveform component, which can also bear signatures of tidal deformability in the progenitor stars, is not shown. Simulations presume a reference BNS coalescence at 100 Mpc. (courtesy J. Veitch and S. Vitale, adapted from Read et al. [31])

## Slide 8: A+ Upgrade Status
NSF awarded US funds, 18 months earlier than original request
  Same end date (4QFY2023, limited by COC coatings) but much faster start
  Acceleration may allow facility and vacuum upgrades between O3 and O4
  Retires risk, may well accelerate commissioning and O5 (no promises!)
  LIGO Lab team has formed and mobilized; formal start in 1 month, 10/1/2018
Australian ARC funding has already been awarded
Companion UK proposal is now under UKRI/STFC review
  We are cautiously optimistic for a similar accelerated UK start
  This would relieve schedule pressure on core optics polishing (sequential fabrication) and suspension design pipelines
Big picture: we expect LIGO will be observing with A+ sensitivity by late 2024

## Slide 9: A+ elevator pitch constraints
An incremental upgrade to aLIGO that leverages existing technology and infrastructure, with minimal new investment, and moderate risk
Target: factor of 1.7* increase in range over aLIGO
About a factor of 4-7 greater CBC event rate
Bridge to future 3G GW astrophysics, cosmology, and nuclear physics
Stepping stone to 3G detector technology
Can be observing within 6 years (mid- 2024)
“Scientific breakeven” within 1/2 year of operation
Incremental cost: a small increment on aLIGO
*BBH 30/30 M: 1.6x
*BNS 1.4/1.4 M: 1.9x

## Slide 10: Look at all the constraints:
“Your next investment should…
  …be incremental in cost
  …minimize loss of observing for existing instruments
  …provide immediate scientific return
    e.g., improved rate*time integral should ‘quickly’ wipe out observing hiatus due to upgrade
  …build upon and fully exploit prior investment
    “we already invested 109 $/€/£…”
  …simultaneously support following investments, e.g.,
    test technology for “(n+1)G”
    probe future astro source landscape

## Slide 11: …all the constraints (2):
All good and wholesome, but taken together, recipe for a holding pattern
Nothing big happens that way
  (certainly not Initial or Advanced LIGO)
Which constraints to challenge here?
  (really asking, I don’t know).

## Slide 12: Are there other constraints we should be considering?
For example:
  We naturally fret about seismic, quantum and thermal noise
  Our reviewers (perhaps the more influential ones?) may fret about 15% cost growth in steel, earthmoving, or concrete
    Even “routine” roads and tunnels see 100% overruns
  Are we investing responsibly to bound and manage large, “conventional” risks, or are we only looking after the novel “interesting” ones?

## Slide 13: Suggestion: diversify
Increments like A+, AdV+ and Voyager are necessary, but too overconstrained to put us in the strike zone
Always the possibility of a visionary patron and a leap of faith; hope for this, but can’t plan on it
3G technology demonstration investments can retire investment risks
  Without interfering with 2/2.1/2.5G observations
  Without forcing ‘profitable’ integration on an existing (obsolete) instrument
LIGO and Virgo invested millions and decades to pre-qualify
  beamtube construction;
  phase noise at the MIT 5m;
  displacement noise at the CIT 40m;
  optic polishing, metrology & coating pathfinders;
  etc.
What are the analogs for 3G?

## Slide 14: Possible “Large-scale” 3G technology demonstration investments
3G Value-Engineered Beamtube Demo
  LIGO is planning a water vapor desorption test on a spare 7m tube section at LLO
  NSF just funded a LIGO workshop for early ‘19 on Very Large Scale Vacuum Systems
  What about a 500m scale 3G beamtube fabrication and degassing test?
3G Tunnel/Earthwork Demonstration
3G Very Large Optic Polishing & Coating Pathfinder
…?...(ideas welcome)

## Slide 15: Discussion points
Nobody wants to wait
Nobody wants to invest 10-100M $/€/£ in engineering demo projects that don’t detect GW’s
BUT
Moving directly to full scale design without some proofs of concept may meet resistance
We can’t demonstrate all of what we need on H1/L1/V1/K1/I1
We probably need to break all the risky problems (not just the interferometry) into pieces and show what we can do in each domain separately.
We hope that increments like A+, AdV+, and Voyager will buy us time and let us hold our place at the forefront of modern astrophysics

## Slide 16: THANKS (and sincere apologies from MZ)

## Slide 17: Spare Slides

## Slide 18: A+ WBS & foreign effort
UK ISC
  BHD readout
UK COC
  Large beamsplitter
  COC substrates, polish, coatings
UK SUS
  BOSEMs
  BHD SUS
  Large BS SUS
UK CDS
  Coil drivers (partial)
AUS ISC
  SQZ optics (partial)
  Adaptive mode match (partial)

## Slide 19: A+ Proposal Team
LCCL- Zucker
  Science targets- Vitale
Lead Engineer- Billingsley
Project Manager- Hansen
  Schedule & resources- Toon
Subsystem Leads:
  Systems- Torrie
  Core Optics- Billingsley
  Seismic- Mason
  Suspensions- Robertson
  Facilities- Oram
  Vacuum- Romel
  CDS- Abbott
  ISC- Barsotti
UK
  Lead- Strain
  Science Case- J. Veitch
  ISC (BHD)- Hild
  SUS- O’Dell
  COC- Hammond
Australia
  Lead- McClelland
  ISC- McClelland, P. Veitch
(CIT and MIT departments covered US proposal prep costs )

## Slide 20: A+ NSF Proposal Review: Panel Summary
“Over the last several years LIGO has made tremendous discoveries which have inspired people around the world and demonstrated the value of gravitational-wave observation as a new tool for astronomy. The proposed effort promises to make a major advance in that effort for even better science. The proposed technical improvements take careful aim at the dominant noise sources remaining at the aLIGO design sensitivity, with a very carefully thought through approach, deploying cutting-edge technological innovations with careful thought to mitigating risks of delay and/or lost science opportunity. While some minor concerns are described in the section notes these are far outweighed by the overwhelming strengths of the proposal. The panel strongly recommends funding the proposed upgrade.”

## Slide 21: A+ parameters vs. aLIGO

## Slide 22: Improved Mirror Coatings for A+
TARGET: Elastic loss angle φ < 9 x 10-5
  (aLIGO φ = 3.6 x 10-4)
Current R&D on small samples
UK, Europe and US Center for Coatings Research initiative to select best low-loss coating design in about 2 years
A+ Coating Pathfinder program will spin up industrial vendor(s) and qualify full-aperture coatings for production
In parallel, new and existing spare aLIGO optics will be polished
Metrology, QA, lab infrastructure, tooling, procedures all same as aLIGO & reused
Replacement core optics delivered for final phase of A+ installation (mid-FY23)
400mm LIGO Fizeau
interferometer at CIT
aLIGO ETM figure map
6.5 ÅRMS over central 160 mm Φ
(LIGO Lab/G. Billingsley)

## Slide 23: A+ Coatings
A+ goal
Gras & Evans, P1700448

## Slide 24: Quantum Noise Reduction for A+: Frequency-Dependent Squeezing
Expect squeezed light injection to be operating soon
Effective substitute or assist for high laser power
  Phase squeezing at HF causes amplitude anti-squeezing (radiation pressure) at LF
  Added radiation pressure bothersome as other LF noise is improved
Solution: Frequency-dependent squeezing (FDS)
  NOTE: FDS is also key for planned future detectors (Voyager, ET, CE, etc.)

## Slide 25: Frequency-Dependent Squeezing
Optical “filter cavity” (FC)
Rotates squeezing phase to both improve radiation pressure at LF and phase noise at HF
Low-loss, high finesse cavity with bandwidth ~100 Hz
Sensitive to optical losses, scattering and mirror motion
Requires seismic isolation and quiet mirror suspension
Requires high-quality FC mirrors
Requires LFC ~ 300 m

## Slide 26: FDS demonstration w/ 2m filter cavity
LIGO demonstration of audio-band frequency dependent squeezing
(A+ Proposal figure 3)
Oelker et al, LIGO-P1500062

## Slide 27: Filter cavity vacuum system and facility modifications
50 m
Corner station (Hanford)
50 m
300 m
(TO LLO)
C. Torrie & E. Sanchez

## Slide 28
View from future LLO FC end station back to corner
A+ FILTER CAVITY
BEAMLINE
C. Torrie, E. Sanchez , G. Billingsley
M1800040
New HAM
Chamber
New HAM
Chamber
New station
building
New 20cm
Beamtube &
Enclosure

## Slide 29
A+ filter cavity:
mirror suspension & seismic isolation
aLIGO HAM Small Triple Suspension (HSTS)
aLIGO HAM Internal Seismic Isolator (HAM-ISI)
Notes: HAM ISI insertion in HAM6 at Livingston with guidance from Jeff Kissel (LSU, left) and Brian O’Reilly (LLO, right). March 2008.

## Slide 30: Balanced Homodyne Readout (UK)
Reduced dark-port loss
Improved backscatter immunity
Improved phase tuning flexibility
Enhanced readout dynamic range
LIGO-P1300184

## Slide 31: Balanced homodyne readout
Revised: LO DIFFERENTIAL PHASE NOISE IS CRITICAL!
Need low-noise beam relay mirrors
OMC’s now after LO/AS interference
LIGO-P1300184

## Slide 32: A+ BHR LO beam relay (work in progress)
POP pickoff beam used for homodyne local oscillator
LO phase noise critical
Requires sub 10-18 m/Hz1/2 mirror noise at 100 Hz
Triple-stage suspension for relay optics
Space constraints  new compact triple suspension design is required

## Slide 33: A+ Technical Updates
Filter cavity length  300m
    Model showed insufficient backscatter margin at 100m
    Modest hit in civil & vacuum cost
Low-noise relay optics for BHD local oscillator
    Models revealed enhanced phase noise susceptibiity
    Now baselining ~ 11 triple-pendulum suspended small optics to deliver low-noise LO beam (new design)
    US to do design, UK to fund production
BHD topology changed
    AS and LO beams to be interfered before mode cleaners
    Modified OMC suspensions needed
Anticipating coating progress…
    Looking closely at zirconia-doped tantala

## Slide 34: Observing scenario
From P1200087-v47

## Slide 35: Original simplified schedule
From ‘19-23 LIGO ops renewal proposal

## Slide 36: Sample revised schedule (schematic)
Advance civil & vacuum construction to O3-O4 break
Start optics integration immediately at end of O4
Installation A
Installation B
A+ award

## Slide 37: Context: Bridging the Gap (adapted from G1401081)
Advanced LIGO
Si, Cryo, 2 µm R&D
LIGO Voyager – Current Facility
Ultimate Detector R&D
ET, CE--New Facility
?
time
aL Design Target (±)
2027?
2037?
2017
It may take a decade for “next-generation” GW instrument technology to come online.
Is extended observation at aLIGO performance limits the best we can do?

## Slide 38
“New” FC HAM chambers (HAM7,8) salvaged from H2
New HAM ISI and HSTS for FC mirrors
LO beam relay to use new “HRTS” triple suspension for low phase noise
BHD OMC’s may use a common suspended platform (based on VPI)
FC pipe penetrates BSC3 (beam passes behind ITMX)
C. Torrie & E. Sanchez

## Slide 39: A+ target noise budget
Barsotti et al, T1800043

## Slide 40: aLIGO Design Target

## Slide 41: A+ Design Target

## Slide 42: A+ FDS with no CTN improvement