## Slide 1: Understanding Interferometer Lock Losses with Machine Learning
Laurel White, Syracuse University
Mentor: Jamie Rollins, California Institute of Technology

## Slide 2: What is a lock loss?
Detectors must be in a stable state known as “lock” in order to collect data
In lock, there is:
  Resonance in each of the cavities
  Destructive interference at the output
The automated lock acquisition system, Guardian, is used to obtain lock, but it is a time-consuming process
A detector can be knocked out of lock, reducing its duty cycle
Some lock losses are caused by earthquakes, while others have unknown causes

## Slide 3: Our approach
Besides the differential arm (DARM) channel which records gravitational-wave signals, there are thousands of auxiliary channels recording information about the detectors and their environments
  Ex. SUS, PEM
Our goal is to identify features in the auxiliary channel data that are characteristic of impending lock loss
  Ex. Large spikes, unstable oscillations
We want to use a regression algorithm to identify the most interesting features and channels out of thousands that we test and then a clustering algorithm to group lock losses with common features

## Slide 4: Our approach
Compile extracted features into matrix X
Use positive/negative labels to generate output vector y
Solve for w, which maps X onto y
Courtesy of Jamie Rollins

## Slide 5: Overview
Generating the dataset
Methods and results
  Feature extraction
  Regression
  Clustering
  Follow-up of interesting results
Conclusions and future work

## Slide 6: Generating the dataset
Use O2 data from Hanford
Channels: start with DQ channels, remove calibration channels, flat channels, and channels created during O2
Positive samples: just prior to lock losses that occurred during observing mode
Negative samples: stable, locked times spaced by 10,000 seconds and 1,000 seconds removed from the start and end of lock
Sample length is a tunable parameter (we use 4 seconds)
Left with 4,338 channels, 276 positive samples, and 1,086 negative samples

## Slide 7: Approach
Step 1
Feature extraction
Step 2
Regression
Step 3
Clustering

## Slide 8: Approach
Step 1
Feature extraction
Step 2
Regression
Step 3
Clustering

## Slide 9: Step 1: Feature Extraction
Complexity
Take the diff:
Dot with itself
Take square root
Cannot use raw time series data
  Channels are sampled at rates of up to 16,384 Hz
  Too much data would hide interesting features in the regression
We select a set of calculations that return single-value outputs for each sample
  Difference between maximum and minimum
  Complexity
  Absolute energy
  Mean value
  Standard deviation
  Variance
  Kurtosis
  Skewness
  Absolute sum of changes
  Mean absolute change
  Permutation entropy

## Slide 10: Approach
Step 1
Feature extraction
Step 2
Regression
Step 3
Clustering

## Slide 11: Step 2: Regression
Matrix is underdetermined, so we use Lasso regression
  Alpha parameter controls degree of regularization
  Use of L1-norm drives some coefficients to be zero so final model relies on less features
Courtesy of Jamie Rollins
Ordinary least squares

## Slide 12: Step 2: Regression
Matrix is underdetermined, so we use Lasso regression
  Alpha parameter controls degree of regularization
  Use of L1-norm drives some coefficients to be zero so final model relies on less features
Courtesy of Jamie Rollins
Ordinary least squares
Regularization
L1 norm
(Lasso)

## Slide 13: Step 2: Regression
Use receiver operator characteristic (ROC) curves with area under the curve (AUC) scores as well as histograms to evaluate success of regression
Complexity of H1:OMC-FPGA_DTONE_IN1_DQ

## Slide 14: Approach
Step 1
Feature extraction
Step 2
Regression
Step 3
Clustering

## Slide 15: Step 3: Clustering
Attempt to cluster samples to find groups of lock losses that share common features
K-means algorithm groups into any specified number of clusters
No built-in functionality to figure out which features are most important for clustering
http://shabal.in/visuals/kmeans/6.html
X-axis
Y-axis

## Slide 16: Step 3: Clustering
Ideally would see clear clusters in histograms
Complexity of H1:OMC-FPGA_DTONE_IN1_DQ

## Slide 17: Step 3: Clustering
Ideally would see clear clusters in histograms
Complexity of H1:OMC-FPGA_DTONE_IN1_DQ

## Slide 18: Step 3: Clustering
Ideally would see clear clusters in histograms
Complexity of H1:OMC-FPGA_DTONE_IN1_DQ

## Slide 19: Follow-Up: H1:OMC-FPGA_DTONE_IN1_DQ
When we plot the ASDs, we see that positive samples tend to have peaks at lower frequencies than negative samples
This does not explain the higher complexity values for the positive samples

## Slide 20: Follow-Up: H1:OMC-FPGA_DTONE_IN1_DQ
When we plot the ASDs, we see that positive samples tend to have peaks at lower frequencies than negative samples
This does not explain the higher complexity values for the positive samples

## Slide 21: Follow-Up: H1:OMC-LSC_DITHER_OUT_DQ
The permutation entropy always hovers around one value for the negative samples, but it is split between two values for the positive samples

## Slide 22: Follow-Up: H1:OMC-LSC_DITHER_OUT_DQ
Plotting the ASDs shows no pattern among the noise levels for the positive or negative samples, regardless of the values of the permutation entropy
Both samples have high permutation entropy
The positive sample has low permutation entropy

## Slide 23: Conclusions
Identified a small number of interesting features which differ between lock loss and clean times
Did not find meaningful clusters
Future work
Prune channel list
Find new features that better distinguish positive from negative samples
Refine clustering

## Slide 24: References
Evans, M., et al. (2002). Lock acquisition of a gravitational-wave interferometer. Optics Letters, 27(8).
Rollins, J. (2015, June 16). Advanced LIGO Guardian Documentation, Release 1447. Retrieved from https://dcc.ligo.org/public/0120/T1500292/001/AdvancedLIGOGuardian.pdf
Rollins, J. (2017, July 20). Machine learning for lock loss analysis. Retrieved from https://dcc.ligo.org/public/0144/G1701409/001/main.pdf.
Documentation of scikit-learn 0.20.3. (2018). Retrieved from https://scikit-learn.org/stable/documentation.html
Documentation of tsfresh. (2019). Retrieved from https://tsfresh.readthedocs.io/en/latest/
Documentation of EntroPy. (2019). Retrieved from https://raphaelvallat.com/entropy/build/html/index.html

## Slide 25: Acknowledgements
My mentor, Jamie Rollins
The LIGO SURF program and NSF
My fellow SURF students
Thank you! Questions?