## Slide 1: Status of LIGO Hanford Observatory
GWANW
29 June 2020
Zzzz

## Slide 2: Sensitivity Improvement in O3
Noise subtraction not yet done for O3b
Early O3a
Late O3b

## Slide 3: Improvements During O3
Automated running – no overnight shifts
Wind fence (53871, 55971)
R0 tracking (54556)
Squeezer fiber fixed – more squeezing (52675)
SR3 heater tuning – mode matching (48406)
Earthquake mode auto transition (56170, 55347)
Using 2 photodiodes for CARM to reduce shot noise (48762)
Power Recycling Cavity Length Feedforward (51553)
Decoupling Length/Angle (51717)
Change DARM offset (55264)
Eliminate 48 Hz peak (52184)
Frequency dependence of squeezing (56068)
Testing Newtonian Calibrator (53819)
CPS diff for robustness (53390)
(71% Observing in O3a)

## Slide 4: PRCL Feedforward
Alog 51553
Coherence reduced in GW band when PRCL FF engaged
Does make noise slightly worse around 10 Hz, but that is out of GW band

## Slide 5: Differential Seismic
Pink on, green off
May be leading to excess glitches (ongoing study, ex. 56080)
Should give improvement to robustness, esp to earthquakes and wind
Lower DARM with “CPS DIFF” engaged
Alog 53390

## Slide 6: Wind Fence
Alog 53871
Alog 55971
Reduce wind speed at end buildings
Improve robustness, duty cycle
Some improvement in glitches

## Slide 7: LHO Noise Budget O3b
Alog 56195

## Slide 8: From Unlocked to Observing
Video by Kai Staats

## Slide 9: Toward O4
Even more stray light control baffles (eg. Suspended transmission benches, LHO output Faraday)
- May be deferred due to time constraints
New higher power laser
Swap last test mass at LHO – reduce imbalances between arms
Lower loss output Faraday isolator
Frequency dependent squeezing (filter cavity)
Relock H1 after hibernation, check sensitivity esp. after nearby earthquake (6.5 in Idaho)

## Slide 10: Anticipated Sensitivity for O4
From G2000903