## Slide 1
State Estimators for SEI-SUS control
.
Edgard Bonilla, Alec Engl, Brian Lantz
DCC - G2201513

## Slide 2: Outline
Motivation
State Estimators
Roadmap
Results (so far)
Conclusions

## Slide 3: Before we start
How I think I will look:
How I might actually look:

## Slide 4: Outline
Motivation
State Estimators
Roadmap
Results (so far)
Conclusions

## Slide 5: Motivation
Example from SRCL
(From G2001539, G2100193).
ISI motion (below 0.7 Hz)
Coupling from MICH (1-4 Hz)
OSEM noise (4-10 Hz)
We would like to reduce the control bandwidth of the ISC loops.
We need to reduce the noise in auxiliary degrees of freedom.

## Slide 6: Motivation
What do we do with the OSEMs? (simplified)
10 times larger than HAM-ISI motion!
1000 times larger than inertial m1 motion!
Observe and damp resonances

## Slide 7: Motivation
1) Improving the OSEMs
SmarAct (see, for example SWG 11766)
HoQI (see, for example, G2100400)
2) Tuning the damping loops
Things we can do:
3) Using the other sensors we already have:
The HAM-ISI GS13 could potentially be used
to infer the m1 motion with good accuracy
BUT:
We need SUS drive information
Modelling errors can be a nuisance

## Slide 8: Outline
Motivation
State Estimators
Roadmap
Results (so far)
Conclusions

## Slide 9: State Estimators
Sensor measurements
Drives
Mathematical Model
Inferred motion
of the suspension
State Estimator
Especially things that weren’t directly measured
A few options:
Estimator with GS13+drives only.
Kalman Filtering.
Wiener-Hopf filtering.
H-infinity estimators.
Blending OSEMs + (GS13+drives).
Too Many Options!

## Slide 10: State Estimators
Can be used for control (sees the resonances).
Better high-frequency performance than the OSEMs.
Is robust against small modelling errors.
A good enough estimator has (at least) four properties:
Can be translated well into practice
How do we plan to get there?

## Slide 11: Outline
Motivation
State Estimators
Roadmap
Results (so far)
Conclusions

## Slide 12: Roadmap:
Exploration (single SUS model)
  Gain expertise with state estimators
  Identify pitfalls
  Identify opportunities
SEISMIC ISOLATION TABLE
M1
GS13
OSEM

## Slide 13: Roadmap:
Explore (single SUS model)
Prototype (at the Stanford ETF)
  Compare the performance of different estimation techniques
  Sort out the difficulties of implementation.
SEISMIC ISOLATION TABLE
M1
GS13
OSEM
STAGE 2
STAGE 1
CPS
L4C
T240
GS13

## Slide 14: Roadmap:
Explore (single SUS model)
Prototype (at the Stanford ETF)
Complexify (triple SUS model)
  Identify potential differences and pitfalls
SEISMIC ISOLATION TABLE
M1
GS13
OSEM
SEISMIC ISOLATION TABLE
M1
GS13
OSEM
M2
M3

## Slide 15: Roadmap:
Explore (single SUS model)
Prototype (at the Stanford ETF)
Complexify (triple SUS model)
Test (maybe on the Filter Cavity suspensions)

## Slide 16: Outline
Motivation
State Estimators
Roadmap
Results (so far)
Conclusions

## Slide 17: Results (so far)
Learnings from single SUS model
General learnings
  State estimators allow us to do inertial damping.
  We want good velocity estimators

## Slide 18: Results (so far)
Learnings from single SUS model
General learnings
  State estimators allow us to do inertial damping.
  We want good velocity estimators
Kalman Filtering
  Steady state Kalman filtering is good enough.
  Good robustness.

## Slide 19: Results (so far)
Learnings from single SUS model
General learnings
  State estimators allow us to do inertial damping.
  We want good velocity estimators
Kalman Filtering
  Steady state Kalman filtering is good enough.
  Good robustness.
GS13+drives estimator
  Best potential for inertial damping.
  Doesn’t incorporate OSEM information.
  Sensitive to model inaccuracies.

## Slide 20: Results (so far)
Learnings from single SUS model
Other observations
  The closed loop performance looks promising.

## Slide 21: Outline
Motivation
State Estimators
Roadmap
Results (so far)
Conclusions

## Slide 22: In summary:
We have a lot of information on our SUS and SEI systems.
State estimators could use that information to control the suspensions.
We could benefit from trying to damp to inertial space.
There are ‘Good enough’ estimators that only use CDS filters.
We will test these ideas at the prototype facility at Stanford.

## Slide 23: More to do:
Explore (single SUS model)
Try other approaches to sensor fusion. (matrix Wiener-Hopf, H-infinity, etc.)
Combine this with Conor’s particle swarm optimizer for blend filters.
Incorporate more of the HAM-ISI information in the filtering.
System identification to deal with model uncertainty (IIRational, DMD, etc.)
2) Prototype (at the Stanford ETF) [As soon as we’re done with cBRS tests]