## Slide 1
Validating LIGO Interferometer Models
Abhiram Sharma, Cecilia Ochoa, Mary Ranjbar, Xuesi Ma, Jonathan Richardson
LIGO-T2600158
ask40@gatech.edu August 21, 2026

## Slide 2
Commissioning Modeling
LIGO is currently in between observing runs, improved knowledge on discrepant design parameters (such as mirror position displacement) is important
Having an accurate model would help determine how future upgrades would affect the interferometer’s behavior/performance
Present

## Slide 3
Commissioning Goal:
Create a model of the interferometer which can reproduce experimentally measured channel values

## Slide 4
LLO from a Modeling Perspective
LLO is a complicated optomechanical system with hundreds of ports, optics, etc
The physics of the interferometer dictate what we measure from the dozens of detectors/channels
For the purpose of optical modeling, let’s reduce this system into a nonlinear function:
DCC: G1200071

## Slide 5
LLO is a complicated optomechanical system with hundreds of ports, optics, etc
The physics of the interferometer dictate what we measure from the dozens of detectors/channels
For the purpose of optical modeling, let’s reduce this system into a nonlinear function:
Capote, E., et al. , arXiv:2411.14607 (2024)
LLO from a Modeling Perspective

## Slide 6
LLO is a complicated optomechanical system with hundreds of ports, optics, etc
The physics of the interferometer dictate what we measure from the dozens of detectors/channels
For the purpose of optical modeling, let’s reduce this system into a nonlinear function:
Capote, E., et al. , arXiv:2411.14607 (2024)
LLO from a Modeling Perspective
Parameters/Inputs

## Slide 7
LLO is a complicated optomechanical system with hundreds of ports, optics, etc
The physics of the interferometer dictate what we measure from the dozens of detectors/channels
For the purpose of optical modeling, let’s reduce this system into a nonlinear function:
Capote, E., et al. , arXiv:2411.14607 (2024)
LLO from a Modeling Perspective
Detectors/
Outputs

## Slide 8
LLO from a Modeling Perspective

## Slide 9
At high circulating arm power, heating effects from the laser into optics (such as the test masses) significantly alter the cavity mode structure
Heating deformations are compensated by the TCS components, like ring heaters, but this needs to be included into our model
Thermal Dynamics in ITM
Thermal Dynamics in LIGO
Laser Heating
CO2 Laser
Compensation Plate
FROSTI
FROSTI
Surface Deformation
ITM
CO2 Laser
Ring Heater
Compensation
Plate

## Slide 10
LLO Thermal Steady State Data
Segments where the interferometer was locked >24 hours and the TCS components were fixed
Data coming from this period will be much more comparable to a steady state model compared to using the transient regime
~3 hrs

## Slide 11
LLO Thermal Steady State Data

## Slide 12
LLO Thermal Steady State Data
Input Laser Power

## Slide 13
Commissioning Model Results
This comparison table shows the agreement with the FINESSE model and experimental values after calibration
FINESSE
Detector
FINESSE
Output (W)
LLO
Output (W)
LLO
Channel (cts)
Channel
Calibration (W/ct)
Gain (Unitless)
(mW)
(mW/mA)

## Slide 14
SURF Project Goal:
Diagnosing discrepancies between model and experimental results with MCMC sampling

## Slide 15
*Parameter Estimation for the Interferometer Instead of Black Holes
Abhiram Sharma, Cecilia Ochoa, Mary Ranjbar, Xuesi Ma, Jonathan Richardson
LIGO-T2600158
ask40@gatech.edu August 21, 2026

## Slide 16
MCMC parameter estimation
Implementing Markov chain Monte Carlo (MCMC) sampling into the FINESSE commissioning model allows us to estimate the posteriors of various parameters
The emcee python package was chosen for sampling
Posterior
Prior
Likelihood
arxiv: 1202.3665

## Slide 17
MCMC parameter estimation
Emcee’s main sampling methods are affine invariant (unchanged by location-scale transformations)
This means we don’t have to choose a characteristic scale for every parameter
arxiv: 1202.3665, 2605.30412

## Slide 18
MCMC parameter estimation
TRUE PARAMETER VALUES
(ETM RH Power, PR2 dX)
Measurement Uncertainty
FINESSE Model Parameter Values
(Encoded in Prior)
FINESSE Detector Outputs
(Pin, Parm, PX)
Simulation
LLO Detector Outputs
(L1:LSC-POP_A_LF_OUTPUT)
Calibration Uncertainty
+
Sensing
Noise

## Slide 19
MCMC parameter estimation - Cold Model
My initial implementations for the sampler were tested on simple LLO cold models, provided in the finesse-ligo package

## Slide 20
MCMC parameter estimation - Cold Model

## Slide 21
MCMC parameter estimation - Cold Model
Corner plot showing posterior distribution of radius of curvatures of ITM vs ETM in X arm
Unrealistically low 1 sigma values for prior distribution leads to narrow uncertainty

## Slide 22
MCMC parameter estimation - Cold Model
Modifying the sampler to eventually work directly with experimental data also means only using detectors we have calibration factors for
This significantly reduces the amount of information we can obtain from a parameter perturbation
76 Detectors
10
Detectors

## Slide 23
MCMC parameter estimation - Cold Model
Loss in RoC correlation due to removal of certain field detectors and power detectors

## Slide 24
MCMC parameter recovery
Perturbed PARAMETER VALUES
(ETM RH Power - 0.1W,
PR2 dX + 0.1 mm)
Measurement Uncertainty
FINESSE Model Parameter Values
FINESSE Detector Outputs Given Proposed Θ
(Pin, Parm, PX)
Simulation
LLO Detector Outputs
(L1:LSC-POP_A_LF_OUTPUT)
Detector Uncertainty
(Generate data vector)

## Slide 25
MCMC parameter recovery - Sensitivity
We can gauge how sensitive the detectors in the model are to parameters by comparing posterior width to prior width
(Constraining power/informativeness)
Unchanged detectors are insensitive
Decreased detectors are sensitive

## Slide 26
MCMC parameter recovery - Accuracy
We can also gauge the accuracy of the sampler by perturbing where the initial data is generated from
If the sampler starts with prior means far from these perturbed true values, and is able to recover the perturbed values in the posterior distribution, the sampler can accurately recover those parameters
(Bias/Injection-Recovery)

## Slide 27
MCMC parameter recovery - PRC Mirror Displacements

## Slide 28
MCMC parameter recovery - PRC Mirror Displacements

## Slide 29
MCMC parameter recovery - PRC Mirror Displacements
Model is sensitive to PRC mirror displacements (uncertainty shrinks from 0.5 mm to 0.34 mm)
Model can accurately recover the true mirror displacement

## Slide 30
Conclusions
We have developed a diagnostic sampler that can recover certain LLO design parameters given a thermal steady state dataset
We are currently sampling ~10 parameters at a time

## Slide 31
Future Work
Running the sampler with the calibrated experimental data to recover experimental design parameter posterior distributions
Adding further complexity into the sampler/model
Running more stringent, repeated tests to validate sampling methods
Code is currently maintained in this repo: https://git.ligo.org/IFOsim/ligo-commissioning-modeling/

## Slide 32
Acknowledgements
I would like to thank my graduate student mentors and
Dr. Richardson for all their support during the LIGO SURF program.
I also want to acknowledge the support of the NSF, UCR, the LSC, Dr. Barry Barish, and the Caltech LIGO SURF program for making this experience possible.

## Slide 33
Appendix - Locking
Ensuring that the 0th order mode (HG00) is at 0 Hz DC
As we change parameters farther from an initial model’s nominal values, the locking process will take more iterations, or possibly not converge
Locking iterations are a significant fraction of runtime, so minimizing this is important

## Slide 34
Appendix - Thermal Dynamics in LIGO
Surface Deformation

## Slide 35
Appendix - Thermal Dynamics in LIGO
Surface deformations in ITMX due to self heating
Hello Vinet (HV) analytical implementation is what is used in sampling

## Slide 36
Appendix - MCMC Convergence

## Slide 37
Appendix - MCMC parameter estimation
To prevent numerical underflow during computation, we evaluate the non-normalized posterior in log-space:
Log Prior
Log Likelihood
Log Posterior
arxiv: 1202.3665, 2605.30412

## Slide 38
Appendix - MCMC parameter estimation - Cold Model
True Data Vector
FINESSE Output
We construct the log-likelihood using a χ2 statistic:

## Slide 39
Appendix - Sampling Move
We chose to implement a (80/20) combination of the DE move and Snooker move, since this shortened convergence time for correlated posteriors
Snooker Move
DE Move
arxiv: 1202.3665, 2605.30412

## Slide 40
MCMC parameter recovery - Ring Heater Power

## Slide 41
MCMC parameter recovery - Ring Heater Power

## Slide 42
MCMC parameter recovery - Ring Heater Power
Model is more sensitive to ITM RH Power (lower uncertainty)
With chosen systematic error and prior uncertainty, we are currently unable to accurately recover the RH power